## Slide 1: MIP 3H: Centralization Effect on Production Casing Stand-Off
Aan Austin

## Slide 2: Production Cement Placement
Fluid Sequence
Production Shoe Depth = 13,925’
100 bbl of MUDPUSH Express Spacer
Lead FlexSEAL 15 ppg TOC: 1,500’
Tail Slurry 15.4ppg TOC: 6,300’ (KOP)
Three Different Size of Centralizers:
7 7/8 in OD
8 1/4 in OD
8 1/2 in OD
Simulation was done on gauge hole

## Slide 3: 1/1 Cent/Joint – 7 7/8 in OD
Pipe Standoff
Cement Coverage
Min standoff in vertical = 65%
Min standoff in curve = 5 - 45%
Min standoff in lateral = 45%

## Slide 4: 1/1 Cent/Joint – 8 ¼ in OD
Min standoff in vertical = 75%
Min standoff in curve = 16 - 55%
Min standoff in lateral = 57%
Pipe Standoff
Cement Coverage

## Slide 5: 1/1 Cent/Joint – 8 ½ in OD
Min standoff in vertical = 80%
Min standoff in curve = 20 – 60%
Min standoff in lateral = 65%
Pipe Standoff
Cement Coverage